## Slide 1: Introduction to colocalisation analysis

## Slide 3
4 Teams
6 Quizzes - 11 Points in Total
2 Challenges - 14 Points in Total

## Slide 4: What do we mean by colocalisation?

## Slide 5: What do we mean by colocalisation?
Typically refers to one of two things:
  Biologists’ Definition: Co-occurrence of two or more proteins
  Statisticians’ Definition: Correlation of two fluorescent signals
A
B
Chart: Fluorescence Intensity

## Slide 6: Biologists’ assessment often visual
Simplest Case:
  Merge two fluorescence pseudo-coloured images
  Assess whether different wavelengths are present in same pixels
    E.g. Red + Green = Yellow
  Problem:
    Intermediate colour (e.g. yellow) only visible if probes overlap in similar proportions

## Slide 7: “Colour” is highly subjective

## Slide 8
Which nucleus is brighter?
Same Intensity

## Slide 10: Quiz 1: For 1 Point, How many colours Are There?

## Slide 11: Co-Occurance never actually happens!
4x
8x
16x
There is no such thing as “colocalisation”!

## Slide 12: what if DOTs overlap at max resolution?
Fluorophores reside within same volume.
Volume at least one order of magnitude larger than protein complexes

## Slide 13: To put that in perspective…
Imaging volume in confocal microscopy approx. 250 x 250 x 750 nm
Imaging volume can accommodate 2,500 GFP molecules!
24 Å
42 Å

## Slide 14: Correlation is not causation
Colocalisation does not imply interaction
Non-colocalisation probably implies no interaction
Dividing line between colocalisation and non-colocalisation is arbitrary
Extent of colocalisation decreases with increasing spatial resolution
Chart: Spatial Resolution
| 1 | 2 | 3 | 4
Y-Values | 4 | 3 | 2 | 1
Demmerle et al., Nat Protocols, 2017
Relative Localisation
Correlation Analysis

## Slide 15: Quiz 2
For 1 point, which of the following determines the resolution of an image?
Magnification
Image size
Pixel size
Microscope type (widefield, confocal, light-sheet, etc.)
None of the above

## Slide 16: “Colocalisation” means different things to different people
Red + Green = Yellow?
Co-occurrence:
  Molecules present in a region
  No concentration relationship
Correlation analysis:
  Stoichiometric relationship between molecules
  No spatial information
A
B
Chart: Fluorescence Intensity

## Slide 17: Common sources of error

## Slide 18: Potential pitfalls
Probes:
Signal is sufficient to distinguish from noise and background
Uncontaminated by auto-fluorescence
Free of signal bleed-through
Image:
No lossy compression
Not saturated / clipped / overexposed
Spatial resolution sufficiently high

## Slide 19: Avoiding bleed-through
Emission
Filter
https://searchlight.semrock.com/
GFP
RFP
Excitation
Filter
GFP
RFP
Maximizing excitation and emission collection should be balanced with minimizing bleed-through

## Slide 20: Chromatic aberration
Waters, JCB, 2009

## Slide 22: What is Quantitative Colocalisation?
Dunn et al., Am J Physiol Cell Physiol, 2011
“Under the conditions of proportional co-distribution, points of the scatterplot cluster around a straight line, whose slope reflects the ratio of the fluorescence of the two probes.”

## Slide 23
Two criteria must be met:
  Co-occurrence - spatial overlap of probes
  Correlation - probes are co-distributed
Distribution may overlap, but not proportionally
  DAPI will overlap with nuclear proteins, but will unlikely be proportional

## Slide 24: COLOC2 – FIJI Plugin for colocalisation analysis

## Slide 25: The Importance of controls

## Slide 26: Controls
Correlation coefficients mean little in isolation
  Analyses should include positive and negative controls
But, control samples may not exist
  Practical alternative: generate a “random” distribution by scrambling, translation or rotation.

## Slide 27: Generating controls
P = -0.06
P = 0.95
Original
Rotated 90°
Randomised
P = 0.00

## Slide 28: Things to consider when generating controls
P = 0.95
Original
Random Noise
P = 0.00
Spatial Autocorrelation: the value of one pixel is likely to be similar to that of its neighboring pixels.
Most indicate a block size should be the size of the PSF
  Should equal or exceed the size of the objects in an image

## Slide 29
Crick Advanced Light Microscopy ● SW302 ● david.barry@crick.ac.uk

## Slide 30: Useful References
https://dx.doi.org/10.1083/jcb.200903097
https://dx.doi.org/10.1073/pnas.1711314115
https://dx.doi.org/10.1152/ajpcell.00462.2010
https://doi.org/10.1111/j.1365-2818.2006.01706.x
https://doi.org/10.1529/biophysj.103.038422
https://doi.org/10.1242/jcs.211847
https://doi.org/10.1371/journal.pone.0111983
https://doi.org/10.1038/nmeth.3587