## Slide 1: Introduction to colocalisation analysis Part 2

## Slide 2: What do we mean by colocalisation?

## Slide 3: What do we mean by colocalisation?
Typically refers to one of two things:
  Biologists’ Definition: Co-occurrence of two or more proteins
  Statisticians’ Definition: Correlation of two fluorescent signals
A
B
Chart: Fluorescence Intensity

## Slide 4: Biologists’ assessment often visual
Simplest Case:
  Merge two fluorescence pseudo-coloured images
  Assess whether different wavelengths are present in same pixels
    E.g. Red + Green = Yellow
  Problem:
    Intermediate colour (e.g. yellow) only visible if probes overlap in similar proportions

## Slide 5: Correlation is not causation
Colocalisation does not imply interaction
Non-colocalisation probably implies no interaction
Dividing line between colocalisation and non-colocalisation is arbitrary
Extent of colocalisation decreases with increasing spatial resolution
Chart: Spatial Resolution
| 1 | 2 | 3 | 4
Y-Values | 4 | 3 | 2 | 1
Demmerle et al., Nat Protocols, 2017
Relative Localisation
Correlation Analysis

## Slide 6: What is Quantitative Colocalisation?
Dunn et al., Am J Physiol Cell Physiol, 2011
“Under the conditions of proportional co-distribution, points of the scatterplot cluster around a straight line, whose slope reflects the ratio of the fluorescence of the two probes.”

## Slide 7: Intensity-based correlation coefficients
Pearsons
  Analysis of signal correlation
Spearmans
  Similar to Pearsons
  Less sensitive to outliers
Manders
  Analysis of signal overlap
Chart: Red

## Slide 8: COLOC2 – FIJI Plugin for colocalisation analysis

## Slide 9: Background causes spurious results
Dunn et al., Am J Physiol Cell Physiol, 2011
Quantification of PCC within cells indicates poor association (PCC = 0.16)
When quantified over entire image, PCC = 0.39

## Slide 10: Noise results in “Less” correlation
Pcc = 0.41
Pcc = 0.33
Sample can exhibit high co-occurrence, but low correlation

## Slide 11
Mred-green = 0.59
Mgreen-red = 0.68

## Slide 12
Dunn et al., Am J Physiol Cell Physiol, 2011

## Slide 14: Common sources of error

## Slide 15: Potential pitfalls
Probes:
Signal is sufficient to distinguish from noise and background
Uncontaminated by auto-fluorescence
Free of signal bleed-through
Image:
No lossy compression
Not saturated / clipped / overexposed
Spatial resolution sufficiently high

## Slide 16: Avoiding bleed-through
Emission
Filter
https://searchlight.idex-hs.com/
GFP
RFP
Excitation
Filter
GFP
RFP
Maximizing excitation and emission collection should be balanced with minimizing bleed-through

## Slide 17: Chromatic aberration
Waters, JCB, 2009

## Slide 19: Calculating Thresholds

## Slide 21: Quick Refresher on Segmentation
“Background”
“Foreground”
Can be exploited for segmentation

## Slide 22: What is image segmentation?
Process of dividing image into regions
Assigning labels to each pixel
Background
Foreground
“Binary” or “Mask” Image
Foreground labelled black (0)
Background labelled white (255)

## Slide 23: Masks can be black on white or white on black

## Slide 24
FIJI has several variations on this algorithm
Foreground
0
Background
255

## Slide 25
Click “Apply” to generate the binary image

## Slide 26
Masks and ROIS can be considered one and the same

## Slide 28: Costes’ Regression
Costes et al., Biophys J, 2004
Chart: Green
Tr = 200
Tg = 220
Tr = 170
Tg = 180
Tr = 128
Tg = 130
Tr = 70
Tg = 90
Tr = 50
Tg = 50
P>T = 0.90
P<T = 0.60
P>T = 0.80
P<T = 0.45
P>T = 0.70
P>T = 0.60
P>T = 0.50
P<T = 0.30
P<T = 0.15
P<T = 0.00

## Slide 29
This should be close to zero

## Slide 30: Demo 5: Setting Thresholds & Defining Regions

## Slide 31: Quiz 6: Setting Thresholds & Defining Regions
Open the image in the Quiz 6 folder with Bio-Formats:
Use the DAPI channel to define an ROI and measure colocalisation in the other two channels
According to Pearson’s correlation coefficient, what is the extent of colocalisation between channels 2 and 3 within the nuclei?

## Slide 32: Co-occurance Based approaches

## Slide 33: Object-Based colocalisation
Detect objects in different channels and relate positions
  Is signal nuclear or non-nuclear
  Plot distributions from cell boundary

## Slide 34: Object-based correlation coefficients
Detect objects:
  Thresholding
  Local maxima detection
Relate objects:
  % Overlap
But with high resolution, probes may not overlap!
  Nearest Neighbour
  Mean Distance to Other objects
  Cluster analysis
Chart: Red

## Slide 38: Relating different objects
Thresholded Dots
Find Maxima Dots
Nuclear Dots
Non-Nuclear Dots

## Slide 39: Demo 6: Simple differentiation based on regions

## Slide 40: A more refined approach relates distances…
Counting pixels – limited resolution, but fast:
(x1, y1)
(x2, y2)
d
(x1, y1)
1
2
3
(x2, y2)
  Euclidean geometry – computationally intensive:

## Slide 41: Distance Maps
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0
0 | 1 | 1 | 2 | 1 | 1 | 1 | 2 | 1 | 0
0 | 1 | 1 | 2 | 2 | 2 | 2 | 1 | 1 | 0
0 | 0 | 1 | 2 | 3 | 3 | 2 | 1 | 0 | 0
0 | 1 | 1 | 2 | 2 | 2 | 2 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 1 | 2 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 43
Binary Mask
Fluorescent Signal
FIJI will always apply measurements to whatever image is specified here

## Slide 44: Using maps to plot distances
Chart: Distance to Nucleus
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140
 | 15 | 27 | 29 | 29 | 17 | 15 | 10 | 18 | 15 | 9 | 6 | 8 | 5 | 5 | 1

## Slide 45: Demo 7: Calculate relative nuclear expression